## Slide 1
Hydroclimatology for
Water Resources Management (CIVL 7740 T05)
Term project presentation on:
Pre-Seasonal Streamflow Forecasting using a Principal Component Regression Model in the Michipicoten Watershed, Canada
Presented by:
Setogn Abate Getu

## Slide 2
Presentation outlines
      Introduction and Motivation
      Objectives
      Data sources
      Methods and tools
      Methodology and Approach
      Data Analysis
      Results and Discussions
      Conclusions

## Slide 3: Introduction and Motivation
Accurate pre-seasonal streamflow forecasts are essential
The complex interrelationships among hydroclimatic variables are challenging.
The Michipicoten watershed shows significant variability in streamflow forecast due to the complex interactions.
Some prediction methods often struggle with;
      Multicollinearity and
      High dimensionality of climate data
    limiting forecast accuracy
This project aims to provide a reliable forecasts of AMJ streamflow using JFM predictors.

## Slide 4: Objectives
To forecast AMJ streamflow using PCR and MLR based on predictors obtained from early months (JFM)
To identify and rank the most influential predictors for the prediction of AMJ streamflow in the watershed.
Evaluate the model’s performance and reliability using statistical metrics such as Pearson correlation, RMSE, NSE, and MAE.

## Slide 5: Location of Study Area
The Michipicoten River watershed is a large basin draining into northeastern Lake Superior, Ontario, Canada.

## Slide 6: Data sources
Predictand:
Historical streamflow data (1991–2019)
From ECCC (gauge station number 02BD002)
Predictors:
Basin-averaged climate data from the ERA5
Original predictor variables:
      Precipitation (Pr)
      Temperature (T)
      Snow Water Equivalent (SWE)
      potential evapotranspiration(PET)
      Mean sea level pressure (MSLP) and
      Surface Pressure (SP)

## Slide 7: Methods and tools
QGIS; used for shapefile/watershed preparation.
Python: Data processing, analysis and visualization
PCR and CPT : For streamflow forecasting
    PCA applied to handle multicollinearity
    PCs used as a predictor to forecast streamflow.
    AMJ streamflow was forecasted using;
    Model performance : R, RMSE, NSE, and MAE
    The most influential predictors were identified

## Slide 8: Methodology and Approach

## Slide 9: Data Analysis: Correlation between predictors and predictand

## Slide 10
Correlations between combined predictors and streamflow

## Slide 11
Correlation of each predictor with predictand

## Slide 12: Standardization/Normalization

## Slide 13: Results and Discussions
Total Variance Explained

## Slide 14: Results and Discussions
Observed Vs forecasted streamflow (PCR –left Vs MLR-right)

## Slide 15: Results and Discussions
Predictors Influence Ranking -PCR

## Slide 16: Results and Discussions
Scatter plots (PCR –left & MLR-right)

## Slide 17: Contingency table

## Slide 18: Results and discussion
Model performance
Model | RMSE | MAE | Pearson_R | NSE | RPSS
PCR | 25.88 | 22.01 | 0.71 | 0.51 | 0.716
MLR | 30.72 | 25.59 | 0.5953 | 0.31 | 
Regression Equation (PCR Model):
Q_AMJ = 82.361 + (-15.087 * PC1) + (-5.310 * PC2) + (8.455 * PC3)
Regression Equation (MLR Model):
Q_AMJ = 4095.052 -31.31T + 11.4 Pr + 0.35SWE + 10.76PET -135.58MSLP + 1.38SP

## Slide 19: Conclusions
Hindcasted Vs observed streamflow using PCR shows moderate correlation (R=0.712)
The PCR approach effectively overcame the challenge of multicollinearity and provided a more stable forecast than MLR methods.
For PCR, Snow Water Equivalent, precipitation and temperature are the most influential predictors.
PCR model significantly outperformed than MLR model

## Slide 20
Thank you!
Questions?